## Slide 1: Title Slide
Assistive Technology Project

## Slide 2: Introduction
The 3rd Eye project helps blind people detect obstacles.
It uses ultrasonic sensors with Arduino.
A buzzer alerts the user when an object is nearby.

## Slide 3: Objective
• Help visually impaired people move safely
• Detect obstacles using sensors
• Provide alert using buzzer sound

## Slide 4: Components Required
• Arduino Uno
• Ultrasonic Sensor (HC-SR04)
• Buzzer
• Jumper Wires
• Breadboard
• Battery (9V or Power Bank)

## Slide 5: Working Principle
Ultrasonic sensor sends sound waves.
If waves hit an object, they return.
Arduino calculates the distance.
If object is close, buzzer turns ON.

## Slide 6: Circuit Connections
• VCC → 5V (Arduino)
• GND → GND
• TRIG → Digital Pin 9
• ECHO → Digital Pin 10
• Buzzer → Digital Pin 8

## Slide 7: Advantages
• Low cost
• Easy to build
• Portable device
• Helps blind people detect obstacles

## Slide 8: Applications
• Assistive device for blind people
• Smart walking stick
• Obstacle detection systems

## Slide 9: Future Improvements
• Add vibration motor
• Add voice alerts
• Use rechargeable battery
• Add GPS for navigation

## Slide 10: Conclusion
The 3rd Eye system improves mobility for blind people.
It is a simple and effective assistive technology project using Arduino.